## Slide 1: General Assembly Info and Best Practices

## Slide 2: Screws!
Hex
  Screw head doesn’t strip easily
  Bonus: Can use with a ball end hex driver
Phillips
  Very common and easy to find
Notes: Anish

## Slide 3: Head Types
Socket Head
  Common and inexpensive
Button Head
  Flush mounting
Flat Head
  Uncommon on FRC robots
  Used for some electronics
  Used for field elements(made of wood)
Notes: Srini

## Slide 4: Nuts for Screws
Meant to secure material with screw
Nyloc Nut
  Screw that stays in place better
  Nylon collar
Notes: Srini

## Slide 5: Threading
What makes a screw and nut work
  Nuts are made so they can slide into the threading
  NOT ALL SCREWS HAVE THE SAME THREADING!!!
    Different threads per inch(TPI)
    E.g. Metric screw and Imperial screw might seem similar, but they could have different TPIs
Notes: Anish

## Slide 6: Common Screws in FRC
#10-32
  #10 stands for width
  32 is its Threads per Inch(TPI)
#8-32
¼ inch-20
  Width of screw head is ¼ inch
  20 TPI
Notes: Srini